## Slide 1: ECE 5706: Resilient Computer System Design
Resilient Hardware Design – Device-Level
Xin Xin
Assistant Professor
Electrical and Computer Engineering
ACKNOWLEDGEMENT:
Prof. Behrooz Parhami at UCSB
Prof. Ronald F. DeMara at UCF
Notes: <number>

## Slide 2: 1 Defect Avoidance
Slide <number>
Notes: <number>
Defect in a piece of rail, exposed after cutting it.

## Slide 3: 1.1 Types and Causes of Defects
Slide <number>
Resistive open due to unfilled via [R. Madge et al., IEEE D&T, 2003]
Particle embedded between layers
Notes: <number>

## Slide 4: Process and Operational Variations
Slide <number>
Even if there isn’t a complete short or open, resistance and capacitance variations can lead to trouble
Chip temperature map
Notes: <number>

## Slide 5: Analogy: Ideal vs. Real Clock Signals
Slide <number>
Real clock signal is quite different
Ideal clock signal has sharp edges and an exact constant period
Notes: <number>

## Slide 6: Disk Memory Defects
Slide <number>
The tiniest particle or scratch can wipe out many thousands of bits
Notes: <number>

## Slide 7: Protective Error Coding in Disk Memories
Slide <number>
Disks typically use CRC or similarly strong error-correcting codes
It is virtually impossible for data to become contaminated
When a sector repeatedly violates the code, it is assumed to be bad
Bad sectors reduce the disk’s capacity
Disk crashes and other catastrophic failures are a different story
Image credit:
Hitachi
Black: Sector data
Red: Sector code
Blue: Block code
Green: Super-block code
Notes: <number>

## Slide 8: Learning from Failed Disk Drives
Slide <number>
Analyses of failed disk drives have led to the following monitoring suggestions to predict when a disk drive is about to go, thus allowing a preemptive replacement before a hard failure
Head flying height: Downward trend often precedes a head crash
Number of remapped sectors: A bad sector is remapped to a different physical location on disk to avoid repeat errors, so having too many remapped sectors signal persistent problems
Frequency of error correction via the built-in code: Disks routinely use CRC and other coding schemes to protect against data loss, but as errors accumulate, they may go beyond the code’s tolerance limit
The following are signs of mechanical or electrical problems:
- Changes in spin-up time
- Rising temperatures in the unit
- Reduction in data throughput
Notes: <number>

## Slide 9: Solution?
Slide <number>
Spare Component
e.g., the spare component combines the four data components using an XOR operation.
Recovering
Failure
Notes: <number>

## Slide 10: 1.2 Yield and Its Associated Costs
Slide <number>
Notes: <number>
Ciciani, B., Manufacturing Yield Evaluation of VLSI/WSI Systems, IEEE Computer Society Press, 1995.

## Slide 11: Effect of Die Size on Yield
Slide <number>
The dramatic decrease in yield with larger dies
Die yield =def (Number of good dies) / (Total number of dies)
Die yield = Wafer yield  [1 + (Defect density  Die area) / a]–a
Die cost = (Cost of wafer) / (Total number of dies  Die yield)
= (Cost of wafer)  (Die area / Wafer area) / (Die yield)
The parameter a ranges from 3 to 4 for modern CMOS processes
Shown are some random defects; there are also
bulk or clustered defects that affect a large region
Notes: <number>
Note that the product of defect density and die area is the expected number d of defects per die. If this expected number is very small, then, (1 + d/a)^(–a) =approx 1/(1 + d) =approx 1 – d. So, if we expect an average of 0.01 defects per die, say, the yield will be 0.99. For larger values of d, however, nonlinearity kicks in and yield is substantially reduced.

## Slide 12: Effects of Yield on Testing and Part Reliability
Slide <number>
Assume a die yield of 50%
Out of 2,000,000 dies manufactured, 1,000,000 are defective
To achieve the goal of 100 defects per million (DPM) in parts shipped, we must catch 999,900 of the 1,000,000 defective parts
Therefore, we need a test coverage of 99.99%
Testing is imperfect: missed defects/faults (coverage), false positives
Going from a coverage of 99.9% to 99.99% involves a significant investment in test development and application times
False positives are not a source of difficulty in this context
Discarding another 1-2% due to false positives in testing does not change the scale of the loss
Notes: <number>

## Slide 13: 1.3 Defect Modeling
Slide <number>
Defect are of two main types:
Not every spot defect leads to structural or parametric damage
Actual damage depends on location and size (relative to feature size)
Global or gross-area defects are due to:
Scratches (e.g., from wafer mishandling)
Mask misalignment
over- and under-etching
Local or spot defects are due to:
Imperfect process (e.g., extra or missing material)
Effects of airborne particles
Can be
eliminated
or minimized
Harder
to deal with
Notes: <number>
<number>

## Slide 14: Example
Hints?
  AI models can be trained based on characterized systematic defects.
  AI models are often tolerant to small, light errors
Slide <number>
Systematic Defects
  Process Variation
  Can be characterized (predictable)
Random Defects
  Cell-level Defect
  Often unpredictable
Weak / unhealthy blocks due to process variation
Randomly occurred errors
Notes: <number>
<number>

## Slide 15: Is DRAM Reliability a Big Problem in the AI era?
Fault Tolerance in AI Models
  Intrinsic Tolerance to Numerical Approximation
  Only a Small Fraction of Bits Are Highly Critical
  Quantization Can Further Improve Error Resilience
Commodity DRAM Already Has a Very Low Error Rate
  << 10-6
Skanda Koppula, et al, EDEN, MICRO 2019
Slide <number>

## Slide 16: Covered by More Effective System-Level Approaches
System-level reliability mechanisms may already provide sufficient protection against DRAM errors.
Checkpoint
Statistical protection
  Detect errors at runtime using abnormal activation distributions.
Algorithm-based Fault Tolerance (ABFT)
Slide <number>

## Slide 17: Defect Size Distribution
Slide <number>
Sample random defect size distribution, assuming 0.3 defects per cm2
From: http://www.design-reuse.com/articles/10164/model-based-approach-allows-design-for-yield.html
Defect size (nm)
f(x) =
kx–p for xmin < x < xmax
0 otherwise
x = Defect diameter
f(x) = Defect density
k = Normalizing constant
p is typically in [2.0, 3.5]
Notes: <number>

## Slide 18: 1.4 The Bathtub Curve
Slide <number>
Many components fail early on because of residual or latent defects
Components may also wear out due to aging (less so for electronics)
In between the two high-mortality regions lies the useful life period
Time
Failure rate
Infant mortality
End-of-life wearout
Useful life
(low, constant failure rate)
Mechanical
Electronic
Primarily due to latent defects

Notes: <number>

## Slide 19: 1.5 Burn-in and Stress Testing
Slide <number>
From: http://www.weibull.com/hotwire/issue21/hottopics21.htm
Time in years
Percent of parts still working
Burn-in and stress tests are done in accelerated form
Difficult to perform on complex and delicate ICs without damaging good parts
Expensive “ovens” are required
Notes: <number>
Stress testing may include vibration, impacts, drops, and so on.

## Slide 20: Burn-in Oven Example
Slide <number>
From: http://www.goldenaltos.com/environmental_options.html
Notes: <number>
There are companies that offer burn-in service for a fee, so there is no need to purchase an expensive burn-in oven for low production volumes.

## Slide 21: Old chips are not necessarily unreliable
Slow, old chips are often cheaper
Employ slow, old chips as a write-only ECC chip.
Data Chips
ECC Chips
…
3200MT/s
× 4
6400MT/s
× 4 (× 9 chips)
WRITE-ONLY
…
6400MT/s × 4
6400MT/s
× 4 (× 9 chips)
4800MT/s
× 2
and
3200MT/s
× 6
$
$
$
WRITE-ONLY
Employ various slow chips to store parity data with buffer support.
Notes: <number>

## Slide 22: 1.6 Active Defect Prevention
Slide <number>
Other than initial or manufacturing imperfections, defects can develop over the course of a device’s lifetime
Radiation-induced defects
Defects due to shock and vibration
Defects due to mishandling (e.g., scratch or smudge on disk)
. . . discussed in Chap. 7 dealing with shielding and hardening
Defects induced by harsh operating environment
Temperature control
Load redistribution
Clock scaling
Notes: <number>

## Slide 23: 2 Defect Circumvention
Slide <number>
Notes: <number>

## Slide 24: Defect Avoidance vs. Circumvention
Slide <number>
Defect Avoidance
Defect awareness in design, particularly floorplanning and routing
Extensive quality control during the manufacturing process
Comprehensive screening, including burn-in and stress tests
Defect Circumvention (Removal)
Built-in dynamic redundancy on the die or wafer
Identification of defective parts (visual inspection, testing, association)
Bypassing or reconfiguration via embedded switches
Defect Circumvention (Masking)
Built-in static redundancy on the die or wafer
Identification of defective parts (external test or self-test)
Adjustment or tuning of redundant structures
Notes: <number>

## Slide 25: 2.1 Defective Memory Arrays
Slide <number>
Peripheral reconfiguration elements
Defect circumvention (removal)
Provide several extra (spare) rows and/or columns
Route external connections to defect-free rows and columns
Spare rows
Spare rows
Memory
array
Memory
array
Defective row
Defective
column
Defect circumvention (masking)
Error-correcting code
With m rows and s spares,
can model as m-out-of-(m + s)
Somewhat more complex with both spare rows and columns
(still combinational, though)
Modeling with coded scheme has been discussed in prior lectures
Methods in use since the 1970s;
e.g., IBM’s defect-tolerant chip
Spare columns
Spare columns
Notes: <number>

## Slide 26: Standard and spare decoder design
Slide <number>

## Slide 27: 2.2 Defective 1D and 2D Arrays
Slide <number>
Multiple resources on a chip not a challenge if they are independent in logic and I/O connections
Example: To build an MPP out of 64-processor chips, one might place 72 processors on each chip to allow for up to 8 defective processors
Given the probability of a processor (including its external connections) being defective, the chip yield can be modeled as a 64-out-of-72 system
In practice, we interconnect such processors on the chip to allow
higher-bandwidth interprocessor communication and I/O

## Slide 28: Defect Circumvention in Regular Arrays
Slide <number>
Extensive research done on how to salvage a working array from one that has been damaged by defects
Proposed methods differ in
 Types and placement of switches
(e.g., 4-port, single/double-track)
 Types and placement of spares
 Algorithms for determining working
configurations
 Ways of effecting reconfiguration
 Methods of assessing resilience
The next few slides show some methods
based on 4-port, 2-state switches

## Slide 29: Defect Circumvention in Linear Arrays
Slide <number>
A linear array with a spare processor and embedded switching
A linear array with a spare processor and reconfiguration switches
Using 4-port, 2-state switches
Notes: <number>
This and the next few slides are based on Introduction to Parallel Processing: Algorithms and Architectures, by B. Parhami, Plenum Press, 1999.
The scheme shown at the top can be made tolerant to defects in switches and associated interconnects via the provision of two rows of switching elements.

## Slide 30: A Reconfiguration Scheme for 2D Arrays
Slide <number>
A 5  5 working array salvaged from a 6  6 redundant mesh through reconfiguration switching
Seven defective processors
in a 5  5 array and their associated compensation paths

## Slide 31: Highly Redundant Nanoelectronic Memories
Slide <number>
Memory with
block-level redundancy:
Based on hybrid semiconductor/nanodevice
implementation
Error-correcting code applied for defect tolerance, as opposed to operational or “soft” errors
Image source: Strukov/Likharev, Nanotechnology, Jan. 2005
Notes: <number>