## Slide 1: ECE 5706: Resilient Computer System Design
Error Detection & Correction
Xin Xin
Assistant Professor
Electrical and Computer Engineering
ACKNOWLEDGEMENT:
Prof. Behrooz Parhami at UCSB
Prof. Ronald F. DeMara at UCF
Notes: <number>

## Slide 2: Hamming Distance
Part IV – Errors: Informational Distortions
Slide <number>
Definition: Hamming distance between two bit-vectors is
the number of positions in which they differ
Min H-dist Code capability
2 d = 1; SED
3 c = 1; SEC or (d = 2; DED)
4 c = 1 and d = 2; SEC/DED
5 c = 2 or (c = 1 and d = 3; SEC/3ED)
h cEC/dED such that h = c + d + 1
A distance-2 code:
00011
00101
00110
01001
01010
01100
10001
10010
10100
11000
4 3 2 1
Codeword
Correctable
error
Detectable
error
Code-
word
Noncode-
word
00111 (01 error)
00100 (10 error)
d  c, so that d – c represents the add’l detection capability
Notes: <number>

## Slide 3: Error Classification and Models
Part IV – Errors: Informational Distortions
Slide <number>

## Slide 4: Error Detection in Natural Language Texts
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
ERROR
ERROR
ERROR
ERROR
ERROR
ERROR
Erasure errors
EQROR
Substitution error
ERORR
Transposition error

## Slide 5: Application of Coding to Error Control
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
A common way of applying information coding techniques
Arithmetic codes can help detect
(or correct) errors during data manipulations:
1. Product codes (e.g., 15x)
2. Residue codes (x mod 15)
Ordinary codes can be used for storage and transmission errors; they are not closed under arithmetic / logic operations
Error-detecting, error-correcting, or combination codes (e.g., Hamming SEC/DED)

## Slide 6: The Concept of Error-Detecting Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
The simplest possible error-detecting code:
Attach an even parity bit to each k-bit data word
Check bit = XOR of all data bits
Data space: All 2k possible k-bit words
Code space: All 2k possible even-parity (k + 1)-bit codewords
Error space: All 2k possible odd-parity (k + 1)-bit noncodewords
Detects all single-bit errors
Encoding
Decoding
Data words
Codewords
Noncodewords
Errors
Data space
Code space
Error space
0 0 1 0 1 0 0 0 1 1
1
Notes: <number>

## Slide 7: Evaluation of Error-Detecting Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Redundancy: k data bits encoded in n = k + r bits (r redundant bits)
Encoding: Complexity (cost / time) to form codeword from data word
Decoding: Complexity (cost / time) to obtain data word from codeword
Separable codes have computation-free decoding
Capability: Classes of error that can be detected
Greater detection capability generally involves more redundancy
To detect d bit-errors, a minimum code distance of d + 1 is required
Closure: Arithmetic and other operations done directly on codewords
(rather than in 3 stages: decode, operate, and encode)
Examples of code detection capabilities:
Single, double, b-bit burst, byte, unidirectional, . . . errors
Notes: <number>

## Slide 8: 13.2 Checksum Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Ex.: 12-digit UPC-A universal product code—Computing the check digit:
Add the odd-indexed digits and multiply the sum by 3
Add the sum of even-indexed digits to previous result
Subtract the total from the next higher multiple of 10
Checking:
Verify that weighted mod-10 sum of all 12 digits is 0
Example:
Sum odd indexed digits: 0 + 6 + 0 + 2 + 1 + 5 = 14
Multiply by 3: 14  3 = 42
Add even-indexed digits: 42 + 3 + 0 + 0 + 9 + 4 = 58
Compute check digit: 60 – 58 = 2
Bar code uses 7 bits per digit, with different encodings on the right and left halves and different parities at various positions
1 2 3 4 5 6 7 8 9 10 11
Notes: <number>

## Slide 9: Characterization of Checksum Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Given a data vector x1, x2, . . . , xn, encode the data by attaching the checksum xn+1 to the end, such that j=1 to n+1 wj xj = 0 mod A
The elements wj of the weight vector w are predetermined constants
Capabilities:
Detects all errors adding an error magnitude that is not a multiple of A
Checking:
Verify that weighted mod-A sum of all elements is 0
Example:
For the UPC-A checksum scheme, we have
w = 3, 1, 3, 1, 3, 1, 3, 1, 3, 1, 3, 1
A = 10
Variant: Vector elements may be XORed rather than added together
1 2 3 4 5 6 7 8 9 10 11
Notes: <number>

## Slide 10: 13.3 Weight-Based and Berger Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Constant-weight codes
Definition: All codewords have the same number of 1s
Can detect all unidirectional errors
Maximum number of codewords obtained when weight of n-bit codewords is n/2
A weight-2 code:
00011
00101
00110
01001
01010
01100
10001
10010
10100
11000
Notes: <number>

## Slide 11: Berger Codes
Part IV – Errors: Informational Distortions
Slide <number>
Check part
Definition: Separable code that has the count of 0s within the data part attached as a binary number that forms the check part
Alternative – attach the 1’s-complement of the number of 1s
Can detect all unidirectional errors
log2(k + 1) check bits for k data bits
A Berger code:
000000 110
000001 101
000010 101
000011 100
. . .
100111 010
101000 100
. . .
111110 001
111111 000
Jay M. Berger
(IBM)
Notes: <number>

## Slide 12: 13.4 Cyclic Codes
Part IV – Errors: Informational Distortions
Slide <number>
Definition: Any cyclic shift of a codeword produces another codeword
To encode data (1101001), multiply its associated polynomial by G(x)
1 + x + x3 + x6
 1 + x + x3
1 + x + x3 + x6 + x + x2 + x4 + x7 + x3 + x4 + x6 + x9
1 + x2 + x7 + x9
1 0 1 0 0 0 0 1 0 1
A k-bit data word corresponds to a polynomial of degree k – 1
Data = 1101001: D(x) = 1 + x + x3 + x6 (addition is mod 2)
The code has a generator polynomial of degree r = n – k
G(x) = 1 + x + x3
Detects all burst errors of width less than n – k
Burst error polynomial xjE(x), where E(x) is of degree less than n – k
Notes: <number>

## Slide 13: Cyclic Codes: Encoding and Decoding
Part IV – Errors: Informational Distortions
Slide <number>
Encoding: Multiplication by the generator polynomial G(x)
B(x) = (x + x3) D(x) V(x) = D(x) + B(x) = (1 + x + x3) D(x)
Decoding: Division by the generator polynomial G(x)
FF
FF
FF
V(x)
D(x)
x3
x
1
G(x):
FF
FF
FF
V(x)
D(x)
x3
x
1
G(x):
B(x)
Notes: <number>

## Slide 14: Separable Cyclic Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Let D(x) and G(x) be the data and generator polynomials
Example: 7-bit code with 4 data bits and 3 check bits, G(x) = 1 + x + x3
Data = 1 0 0 1, D(x) = 1 + x3
x3D(x) = x3 + x6 = (x + x2) mod (1 + x + x3)
V(x) = x + x2 + x3 + x6
Codeword = 0 1 1 1 0 0 1
Encoding:
Multiply D(x) by xn–k and divide the result by G(x) to get the remainder polynomial R(x) of degree less than n – k
Form the codeword V(x) = R(x) + xn–kD(x), which is divisible by G(x)
Check part Data part
aka CRC = cyclic
redundancy check
Single parity bit:
G(x) = x + 1
Notes: <number>

## Slide 15: 13.5 Arithmetic Error-Detecting Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Unsigned addition 0010 0111 0010 0001
+ 0101 1000 1101 0011
–––––––––––––––––
Correct sum 0111 1111 1111 0100
Erroneous sum 1000 0000 0000 0100

Stage generating an
erroneous carry of 1
How a single carry error can lead to an arbitrary number of bit-errors (inversions)
The arithmetic weight of an error: Min number of signed powers of 2 that must be added to the correct value to turn it into the erroneous result (contrast with Hamming weight of an error)
Example 1 Example 2
------------------------------------------------------------------------ --------------------------------------------------------------------------
Correct value 0111 1111 1111 0100 1101 1111 1111 0100
Erroneous value 1000 0000 0000 0100 0110 0000 0000 0100
Difference (error) 16 = 24 –32752 = –215 + 24
Min-weight BSD 0000 0000 0001 0000 –1000 0000 0001 0000
Arithmetic weight 1 2
Error type Single, positive Double, negative

## Slide 16: Codes for Arithmetic Operations
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Arithmetic error-detecting codes:
Are characterized by arithmetic weights of detectable errors
Allow direct arithmetic on coded operands
We will discuss two classes of arithmetic error-detecting codes, both of which are based on a check modulus A (usually a small odd number)
Product or AN codes
Represent the value N by the number AN
Residue (or inverse residue) codes
Represent the value N by the pair (N, C),
where C is N mod A or (N – N mod A) mod A

## Slide 17: Product or AN Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
For odd A, all weight-1 arithmetic errors are detected
Arithmetic errors of weight  2 may go undetected
e.g., the error 32 736 = 215 – 25 undetectable with A = 3, 11, or 31
Error detection: check divisibility by A
Encoding/decoding: multiply/divide by A
Arithmetic also requires multiplication and division by A
Product codes are nonseparate (nonseparable) codes
Data and redundant check info are intermixed

## Slide 18: Low-Cost Product Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Use low-cost check moduli of the form A = 2a – 1
Multiplication by A = 2a – 1: done by shift-subtract
(2a – 1)N = 2aN – N
Division by A = 2a – 1: done a bits at a time as follows
Given y = (2a – 1)x, find x by computing 2a x – y
. . . xxxx 0000 – . . . xxxx xxxx = . . . xxxx xxxx
Unknown 2a x Known (2a – 1)x Unknown x
Theorem: Any unidirectional error with arithmetic weight of at most a – 1 is detectable by a low-cost product code based on A = 2a – 1

## Slide 19: Arithmetic on AN-Coded Operands
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Add/subtract is done directly: Ax  Ay = A(x  y)
Direct multiplication results in: Aa  Ax = A2ax
The result must be corrected through division by A
For division, if z = qd + s, we have: Az = q(Ad) + As
Thus, q is unprotected
Possible cure: premultiply the dividend Az by A
The result will need correction
Square rooting leads to a problem similar to division
 A2x = A x which is not the same as A  x

## Slide 20: Residue and Inverse Residue Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Represent N by the pair (N, C(N)), where C(N) = N mod A
Residue codes are separate (separable) codes
Separate data and check parts make decoding trivial
Encoding: Given N, compute C(N) = N mod A
Low-cost residue codes use A = 2a – 1
To compute N mod (2a – 1), add a-bit segments of N, modulo 2a – 1
(no division is required)
Example: Compute 0101 1101 1010 1110 mod 15
0101 + 1101 = 0011 (addition with end-around carry)
0011 + 1010 = 1101
1101 + 1110 = 1100 The final residue mod 15

## Slide 21: Arithmetic on Residue-Coded Operands
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Add/subtract: Data and check parts are handled separately
(x, C(x))  (y, C(y)) = (x  y, (C(x)  C(y)) mod A)
Multiply
(a, C(a))  (x, C(x)) = (a  x, (C(a)C(x)) mod A)
Divide/square-root: difficult
Arithmetic processor with residue checking

## Slide 22: 13.6 Other Error-Detecting Codes
Part IV – Errors: Informational Distortions
Slide <number>
Codes for erasure errors
Assume n total symbols, k info symbol, n – m erasures allowed
Info can be recovered from any m symbols in an n-symbol codeword
When m = k, the erasure code is optimal
Codes for byte errors
Bytes are common units of data representation, storage, transmission
So, it makes sense to tie our error detection capability to bytes
Example: Single-byte-error-correcting, double-byte-error-detecting code
Codes for burst errors
With serial data or scratched disk surface, adjacent bits can be affected
Example: Single-bit-error-correcting, 6-bit-burst-error-detecting code
Notes: <number>

## Slide 23: Higher-Level Error Coding Methods
Nov. 2020
Part IV – Errors: Informational Distortions
We have applied coding to data at the bit-string or word level
It is also possible to apply coding at higher levels
Data structure level – Robust data structures
Application level – Algorithm-based error tolerance
Notes: <number>

## Slide 24: Error Correction
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Notes: <number>

## Slide 25: The Concept of Error-Correcting Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
A conceptually simple error-correcting code:
Arrange the k data bits into a k1/2  k1/2 square array
Attach an even parity bit to each row and column of the array
Row/Column check bit = XOR of all row/column data bits
Data space: All 2k possible k-bit words
Redundancy: 2k1/2 + 1 check bits for k data bits
Corrects all single-bit errors (lead to distinct noncodewords)
Detects all double-bit errors (some triples go undetected)
Encoding
Decoding
Data words
Codewords
Noncodewords
Errors
Data space
Code space
Error space
0 1 1 0
0 1 0 1
1 0 1 0
1 0 0 1
0
To be avoided at all cost
Notes: <number>

## Slide 26: Evaluation of Error-Correcting Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Redundancy: k data bits encoded in n = k + r bits (r redundant bits)
Encoding: Complexity (circuit / time) to form codeword from data word
Decoding: Complexity (circuit / time) to obtain data word from codeword
Capability: Classes of error that can be corrected
Greater correction capability generally involves more redundancy
To correct c bit-errors, a minimum code distance of 2c + 1 is required
Combined error correction/detection capability:
To correct c errors and additionally detect d errors (d > c),
a minimum code distance of c + d + 1 is required
Example: Hamming SEC/DED code has a code distance of 4
Examples of code correction capabilities:
Single, double, byte, b-bit burst, unidirectional, . . . errors
Notes: <number>

## Slide 27: Hamming Distance for Error Correction
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Red dots represent codewords
Yellow dots, noncodewords within distance 1 of codewords, represent correctable errors
Blue dot, within distance 2 of three different codewords represents a detectable error
Simultaneous single error correction and double error detection requires that there not be points within distance 2 of some codewords that are also within distance 1 of another
The following visualization, though not completely accurate, is still useful
Notes: <number>

## Slide 28: 14.2 Hamming Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
d3 d2 d1 d0 p2 p1 p0
Data bits Parity bits
Example: Uses multiple parity bits, each applied to a different subset of data bits
Encoding: 3 XOR networks to form parity bits
Checking: 3 XOR networks to verify parities
Decoding: Trivial (separable code)
Redundancy: 3 check bits for 4 data bits
Unimpressive, but gets better with more data bits
(7, 4); (15, 11); (31, 26); (63, 57); (127, 120)
Capability: Corrects any single-bit error
s2 = d3  d2  d1  p2
s1 = d3  d1  d0  p1
s0 = d2  d1  d0  p0
s2 s1 s0 | Error
0 0 0 | None
0 0 1 | p0
0 1 0 | p1
0 1 1 | d0
1 0 0 | p2
1 0 1 | d2
1 1 0 | d3
1 1 1 | d1
s2 s1 s0 Syndrome
Notes: <number>

## Slide 29: Matrix Formulation of Hamming SEC Code
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
d3 d2 d1 d0 p2 p1 p0
Data bits Parity bits
d3 d2 d1 d0 p2 p1 p0
1 1 1 0 1 0 0
1 0 1 1 0 1 0
0 1 1 1 0 0 1
s2 s1 s0 | Error
0 0 0 | None
0 0 1 | p0
0 1 0 | p1
0 1 1 | d0
1 0 0 | p2
1 0 1 | d2
1 1 0 | d3
1 1 1 | d1
Parity check matrix
d3
d2
d1
d0
p2
p1
p0
s2
s1
s0

=
Data bits Parity bits
Syndrome
Received word
Syndrome matches the p2 column in the parity check matrix
Matrix-vector multiplication is done with AND/XOR, instead of /+
Notes: <number>

## Slide 30: Matrix Rearrangement for Simpler Correction
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
p0 p1 d0 p2 d2 d3 d1
Data and parity bits
p0 p1 d0 p2 d2 d3 d1
0 0 0 1 1 1 1
0 1 1 0 0 1 1
1 0 1 0 1 0 1
s2 s1 s0 | Error
0 0 0 | None
0 0 1 | p0
0 1 0 | p1
0 1 1 | d0
1 0 0 | p2
1 0 1 | d2
1 1 0 | d3
1 1 1 | d1
p0
p1
d0
p2
d2
d3
d1
s2
s1
s0

=
Data and parity bits
Syndrome indicates error in position 4
1 2 3 4 5 6 7
Position number
s2
s1
s0
Decoder
0
1-7
Data and parity bits
Corrected version
1-7
1-7
Matrix columns are binary rep’s of column indices
Notes: <number>

## Slide 31: Hamming Generator Matrix
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
d3 d2 d1 d0 p2 p1 p0
Data bits Parity bits
d3 d2 d1 d0
1 0 0 0
0 1 0 0
0 0 1 0
0 0 0 1
1 1 1 0
1 0 1 1
0 1 1 1
Generator matrix
d3
d2
d1
d0

=
Codeword
Data word
d3
d2
d1
d0
p2
p1
p0
Recall that matrix-vector multiplication
is done with AND/XOR, instead of /+
Data bits
Richard W. Hamming
(Bell Labs,
Naval Postgraduate
School)
Notes: <number>

## Slide 32: Generalization to Wider Hamming SEC Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
p0 p1 d0 p2 . . .
0 0 0 . . . 1 1 1
: : : . . . : : :
0 1 1 . . . 0 1 1
1 0 1 . . . 1 0 1
p0
p1
d0
p2
.
.
.
sr1
:
s1
s0

=
Data and parity bits
1 2 3 2r–1
Position number
sr1
:
s1
s0
Decoder
2r1
Data and parity bits
Corrected version
2r1
2r1
n | k = n – r
7 | 4
15 | 11
31 | 26
63 | 57
127 | 120
255 | 247
511 | 502
1023 | 1013
Condition for general Hamming SEC code:
n = k + r = 2r – 1
Matrix columns are binary rep’s of column indices
Notes: <number>

## Slide 33: A Hamming SEC/DED Code
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
1 1 1 . . . 1 1 1 1
0
:
0
0
pr
sr
p0 p1 d0 p2 . . .
0 0 0 . . . 1 1 1
: : : . . . : : :
0 1 1 . . . 0 1 1
1 0 1 . . . 1 0 1
p0
p1
d0
p2
.
.
.
sr1
:
s1
s0

=
Data and parity bits
1 2 3 2r–1
Position number
Add an extra row of all 1s and a column with only one 1 to the parity check matrix
Parity check matrix
Syndrome
Received word
sr1
:
s1
s0
Decoder
2r1
Data and
parity bits
Corrected version
2r1
2r1
sr
q
Not single error
Easy to verify that the appropriate “correction”
is made for all 4 combinations of (sr, q) values
Notes: <number>

## Slide 34: 14.3 Linear Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Hamming codes are examples of linear codes
Linear codes may be defined in many other ways
u = G  d
n-bit codeword
n  k generator matrix
k-bit data word
(Column vector)
Multiplication, with XOR/AND
s = H  v
(n–k)-bit syndrome
(n–k)  n parity check matrix
n-bit suspect word
(Column vector)
Multiplication, with XOR/AND
Notes: <number>

## Slide 35
Slide <number>
A Simple Two-Checksum Protection Code
Encode
Data
[ 3 2 4 5 ]
C₀ = Σxᵢ = 14
C₁ = Σ i·xᵢ = 39
Stored: [ 3 2 4 5 | 14 39 ]
One error
Received
[ 3 2
7
5 ]
(third term: 4 → 7)
C₀′ = 17
C₁′ = 48
Syndrome
Δ₀ = C₀′ − C₀ = 3
Δ₁ = C₁′ − C₁ = 9
j = Δ₁ / Δ₀ = 3
error location
δ = Δ₀ = 3 ⇒ 7 − 3 = 4
error magnitude + correction
Generalization
For a single error xⱼ → xⱼ + δ
Δ₀ = δ
Δ₁ = j·δ
⇒
j = Δ₁ / Δ₀
and δ = Δ₀
Two check values are sufficient to locate and correct one arbitrary symbol error.

## Slide 36: 14.4 Reed-Solomon and BCH Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
BCH codes: Named in honor of Bose, Chaudhuri, Hocquenghem
Reed-Solomon codes: Special case of BCH code
Example: A popular variant is RS(255, 223) with 8-bit symbols
223 bytes of data, 32 check bytes, redundancy  14%
Can correct errors in up to 16 bytes anywhere in the 255-byte codeword
Used in CD players, digital audio tape, digital television
Notes: <number>

## Slide 37: Reed-Solomon Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
With k data symbols, require 2t check symbols, each s bits wide, to correct up to t symbol errors; hence, RS(k + 2t, k) has distance 2t + 1
The number k of data symbols must satisfy k  2s – 1 – 2t (s grows with k)
Generator polynomial: g(x) = (x – )(x – 2)(x – 3)(x – 4);
 is a primitive root mod 7  integers from 1 to 6 are powers of  mod 7 31 = 3; 32 = 2; 33 = 6; 34 = 4; 35 = 5; 36 = 1
Pick  = 3  g(x) = (x – 3)(x – 32)(x – 33)(x – 34)
= (x – 3)(x – 2)(x – 6)(x – 4) = x4 + 6x3 + 3x2 + 2x + 4
k data symbols
2t check symbols
Example: RS(6, 2) code, with 2 data and 2t = 4 check symbols (7-valued)  up to t = 2 symbol errors correctable; hence, RS(6, 2) has distance 5
As usual, the codeword is the product of g(x) and the info polynomial;
convertible to matrix-by-vector multiply by deriving a generator matrix G
Notes: <number>
Code example from: Garrett, P., The Mathematics of Coding Theory, Prentice Hall, 2004, p. 283. For more info, see the website www.4i2i.com/reed_solomon_codes.htm

## Slide 38: Elements of Galois Field GF(23)
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
A primitive element  of GF(23) is one that generates all nonzero elements of the field by its powers
Here are three different representation of the elements of GF(23)
Power | Polynomial | Vector
-- 1  2 3 4 5 6 | 0 1  2  + 1 2 +  2 +  + 1 2 + 1 | 000 001 010 100 011 110 111 101

## Slide 39
Slide <number>
Multiplication table for GF(23)
Addition table for GF(23)

## Slide 40: BCH Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
BCH(15, 7) code: Capable of correcting any two errors
Correct the deficiency of Reed-Solomon code; have a fixed alphabet
We usually choose the alphabet {0, 1}
Generator polynomial: g(x) = 1 + x4 + x6 + x7 + x8
[0 1 1 0 0 1 0 1 1 0 0 0 0 1 0] 
1000 1000
0100 0001
0010 0011
0001 0101
1100 1111
0110 1000
0011 0001
1101 0011
1010 0101
0101 1111
1110 1000
0111 0001
1111 0011
1011 0101
1001 1111
= [x x x x x x x x]
Received word
Parity check matrix
Syndrome
BCH(511, 493) used as DEC code in a video coding standard for videophones
BCH(40, 32) used as SEC/DED code in ATM
Notes: <number>
Example from: Hankerson, R. et al., Coding Theory and Cryptography: The Essentials, Marcel Dekker, 2000, p. 120.

## Slide 41: 14.5 Arithmetic Error-Correcting Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
––––––––––––––––––––––––––––––––––––––––
Positive Syndrome Negative Syndrome
error mod 7 mod 15 error mod 7 mod 15
––––––––––––––––––––––––––––––––––––––––
1 1 1 –1 6 14
2 2 2 –2 5 13
4 4 4 –4 3 11
8 1 8 –8 6 7
16 2 1 –16 5 14
32 4 2 –32 3 13
64 1 4 –64 6 11
128 2 8 –128 5 7
256 4 1 –256 3 14
512 1 2 –512 6 13
1024 2 4 –1024 5 11
2048 4 8 –2048 3 7
––––––––––––––––––––––––––––––––––––––––
4096 1 1 –4096 6 14
8192 2 2 –8192 5 13
16,384 4 4 –16,384 3 11
32,768 1 8 –32,768 6 7
––––––––––––––––––––––––––––––––––––––––
Error syndromes for weight-1 arithmetic errors in the (7, 15) biresidue code
Because all the syndromes in this table are different, any weight-1 arithmetic error is correctable by the (mod 7, mod 15) biresidue code

## Slide 42: Properties of Biresidue Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Biresidue code with relatively prime low-cost check moduli A = 2a – 1 and B = 2b – 1 supports a b bits of data for weight-1 error correction
Representational redundancy = (a + b)/(ab) = 1/a + 1/b
n | k
7 | 4
15 | 11
31 | 26
63 | 57
127 | 120
255 | 247
511 | 502
1023 | 1013
Compare with Hamming SEC code
a | b | n=k+a+b | k=ab
3 | 4 | 19 | 12
5 | 6 | 41 | 30
7 | 8 | 71 | 56
11 | 12 | 143 | 120
15 | 16 | 271 | 240

## Slide 43: Arithmetic on Biresidue-Coded Operands
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Similar to residue-checked arithmetic for addition and multiplication, except that two residues are involved
Divide/square-root: remains difficult
Arithmetic processor
with biresidue checking
D(z)
D(x)
D(y)
s
B
s

## Slide 44: 14.6 Other Error-Correcting Codes
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
Reed-Muller codes: Have a recursive construction, with smaller codes used to build larger ones
Turbo codes: Highly efficient separable codes, with iterative (soft) decoding
Encoder 1
Encoder 2
Interleaver
Data
Code
Low-density parity check (LDPC) codes: Each parity check is defined on a small set of bits, so error checking is fast; correction is more difficult
Information dispersal: Encoding data into n pieces, such that any k of the pieces are adequate for reconstructing the data
Notes: <number>
The two encoders for Turbo codes are generally identical. Soft decoding means that each of two decoders provides an assessment of the probability of a bit being 1. The two decoders then exchange information and refine their estimates iteratively. Turbo codes are extensively used in cell phones and other communication applications.

## Slide 45: Higher-Level Error Coding Methods
Nov. 2020
Part IV – Errors: Informational Distortions
Slide <number>
We have applied coding to data at the bit-string or word level
It is also possible to apply coding at higher levels
Data structure level – Robust data structures
Application level – Algorithm-based error tolerance
Notes: <number>

## Slide 46: Preview of Algorithm-Based Error Tolerance
Part IV – Errors: Informational Distortions
2
1
6
1
5
3
4
4
3
2
7
4
M r =
2
1
6
1
5
3
4
4
3
2
7
4
2
6
1
1
M f =
2
1
6
5
3
4
3
2
7
M =
2
1
6
5
3
4
3
2
7
2
6
1
M c =
Matrix M
Row checksum matrix
Column checksum matrix
Full checksum matrix
Error coding applied to data structures, rather than at the level of atomic data elements
Example: mod-8 checksums used for matrices
If Z = X  Y then Zf = Xc  Yr
In Mf, any single error is correctable and any 3 errors are detectable
Four errors may go undetected